## Slide 1: Computer and Robot vision
Rubik's Cube color detektion
Computer and Robot Vision | Automotive Systems Engineering | WS 24/25

## Slide 2: Agenda
Project description
Challenges of the Project
Process description
Demo-picture
Demo-live

## Slide 3: Project description
The aim is to recognize the 9 coloured squares of a Rubik's cube under different lighting conditions
Experimental setup:
Rubiks cube in grey socket
LED-Lightsource
Webcam

## Slide 4: Challanges
Due to the smooth surface of the cube there a many reflections
The webcam isn‘t mounted in the center of the LED circle which interfers with the exposure
Color correction is limited to small changes in the lighting conditions

## Slide 5: Process description - Flow Chart
Read in Picture/ Frame
Visualize results
Find grey box and crop to ROI
Color correction
Find segments with Edge Detection
Find segments with color filter
Merging of findings
Compensate not detected segments via geometry
Add color information if needed

## Slide 6: Process Description – grey frame detection
Smoothing with bilateral filter
Edge detection with Canny
Closing of edges
Search for largest square contour
Reduce size of outer contour by 5%
Get inner contour by reducing size of outer contour by 10%

## Slide 7: Process Description – color Correction
Calibration to get color conditions of Ground Truth
Ground Truth: Color values of test image, color thresholds based on that
Get RGB-values of grey frame
Calculate correction values
Recalibrate image

## Slide 8: Process Description – color Correction
Before correction
After correction

## Slide 9: Process Description – color filtering
Transform image in HSV color space
Filter image for specified color thesholds
Get contours of object with specified color values
Filter contours based on size, filling factor, squareness
Get attributes for every found object
Notes: Hue, Saturation, Value

## Slide 10: Process Description – color filtering
Mask after color filtering and contour filtering
Notes: Hue, Saturation, Value

## Slide 11: Process Description – Edge Filtering
Get mask of black pixels
Find contours in mask image
Filter contours by area
Calculate focus point of contour
Mask after edge filtering without contour filtering

## Slide 12: Process Description – grid position
Sort focus points of objects in groups of rows and colums
Make sure for three elements in each group
Numbered grid with all fields

## Slide 13: Process Description – Merging of results
Iterate through the grid positions and look for entries in dictionaries
If available in both dicts: Merge with a factorized mean
If grid position only available in one dict: Take that entry
If grid position isn‘t available in any dict: compensate through geometry
Mask after color filtering with one missing object
Mask after edge filtering detection with every object

## Slide 14: Process Description – compensation
Mean x and y groups with three elements each
Look for missing grid position and create dict entry based on centre points
Mask after color filtering with missing objects
Mask after edge filtering detection with missing object
Final image with all objects (compensated sixth tile)

## Slide 15: Process Description – Backwards color det.
Color detection if object detected by Edge detection or Compensation, not by color filtering
Get color values in a rectangle around the focus point of found objects
Compare to extended specified color thresholds, no more filtering by size, filling factor,…
Mask after color filtering with missing objects
Small ROIs in the middle of the tiles to detect the color

## Slide 16: Process Description – Result / Output
Output: Merged dictionary with nine entrys with six keys each
Bounding Box
Focus point
Color
Grid position
Average hue value
Detected way

## Slide 17: Process Description – Result / Output

## Slide 18: Demo via recorded Pictures
Bilder mit verschiedenen Farbeinflüssen

## Slide 19: Limits of the system
Does not work when the cube is rotated in the image
Orange and red color areas are very close to each other, risk of confusion in the border area
Color correction reaches its limits with excessive color deviations
Detection of the grey frame not always exactly at its edge (shadows, angle to the camera)  inaccurate color correction

## Slide 20
Thanks for your Attention